## Slide 1: Exploiting Page Table Locality for Agile TLB Prefetching
georgios.vavouliotis@bsc.es
Georgios Vavouliotis1,2 Lluc Alvarez1,2 Vasileios Karakostas3 Konstantinos Nikas3 Nectarios Koziris3 Daniel A. Jiménez4 Marc Casas1,2
1Barcelona Supercomputing Center
2Universitat Politecnica de Catalunya
3National Technical University of Athens
4Texas A&M University

## Slide 2: Executive Summary
Problem Statement
  Address translation overheads due to data accesses
Our approach —> TLB Prefetching
  Operates on the microarchitectural level
  Relies on the memory access patterns of the application
  Does not disrupt the virtual memory subsystem
Contributions
  Sampling-based Free TLB Prefetching (SBFP)
    Exploit page table locality to enhance TLB prefetching
  Agile TLB Prefetcher (ATP)
    Novel composite TLB prefetching scheme
Combining ATP with SBFP improves geomean performance by more than 10% across different benchmark suites and reduces most of the page walk references to the memory hierarchy

## Slide 3: Outline
Background
Sampling-based Free TLB Prefetching (SBFP)
Agile TLB Prefetcher (ATP)
Methodology
Evaluation
Conclusions

## Slide 4: Address Translation
Each memory access requires a virtual to physical translation
Modern systems provide sophisticated software and hardware support to accelerate address translation
Virtual Address
Address Translation
Physical Address

## Slide 5: x86 Architectural Support for Address Translation
Core
Cache Hierarchy
Page Table
VA1 —> PA17
VA5 —> PA25
Main Memory
PA17
PA25

## Slide 6: x86 Architectural Support for Address Translation
Core
Cache Hierarchy
Page Table
Main Memory
1Intel 5-level Paging, https://software.intel.com/content/www/us/en/develop/download/5-level-paging-and-5-level-ept-white-paper.html
1
PA17
PA25

## Slide 7: x86 Architectural Support for Address Translation
Core
Cache Hierarchy
Page Table
TLB
Main Memory
VA1 —> PA17
VA5 —> PA25
PA17
PA25

## Slide 8: x86 Architectural Support for Address Translation
Core
Cache Hierarchy
Page Table
TLB
Main Memory
PSC
VA1 —> PA17
VA5 —> PA25
PA17
PA25

## Slide 9: Translation Lookaside Buffer (TLB)
Core
Cache Hierarchy
Page Table
Main Memory
VA1 —> PA17
VA5 —> PA25
PSC
L1 I-TLB
L2 TLB
L1 D-TLB
  Last level TLB misses account for most of the cycles spent in the TLB miss handler1
1Basu et. al, “Efficient virtual memory for big memory servers”, ISCA’13
PA17
PA25

## Slide 10: Translation Lookaside Buffer (TLB)
Core
Cache Hierarchy
Page Table
TLB
Main Memory
VA1 —> PA17
VA5 —> PA25
PSC
load VA1
TLB hit
PA17
PA25

## Slide 11: Translation Lookaside Buffer (TLB)
Core
Cache Hierarchy
Page Table
TLB
Main Memory
PSC
load VA1
TLB miss
VA1 —> PA17
PA17
PA25

## Slide 12: Translation Lookaside Buffer (TLB)
Address translation overhead is an emerging problem
**Gras et. al, “Translation Leak-aside Buffer: Defeating Cache Side-channel Protections with TLB Attacks”, SEC’18
**
Chart: 
| Skylake 2015 | BroadwellXeon 2016 | Coffeelake 2017
Region 1 | 212 | 272.4 | 230.3
L2-TLB Miss Penalty (Cycles)
Our analysis indicates that a Perfect TLB3 improves geometric mean performance by up to 70% across different contemporary benchmark suites
3Perfect TLB = ideal TLB where all accesses are hits
2Beamer et. al, “The GAP benchmark suite”, CoRR’15
1XSBench, https://github.com/ANL-CESAR/XSBench
Address translation poses severe performance penalties, especially for big data applications1,2

## Slide 13: TLB Prefetching
Core
Cache Hierarchy
Page Table
TLB
Main Memory
Prefetch
Queue
TLB Prefetcher
Queue
VA1 —> PA17
load VA1
TLB prefetchers use a Prefetch Queue (PQ) to store the prefetches1
1G. B. Kandiraju and A. Sivasubramaniam, "Going the Distance for TLB Prefetching: An Application-driven Study", ISCA'02
TLB Hit!

## Slide 14: TLB Prefetching
Core
Cache Hierarchy
Page Table
TLB
Main Memory
Prefetch
Queue
TLB Prefetcher
Queue
load VA1
Demand Page Walk
Miss!
Hit!
Prefetch Page Walk
TLB Miss!

## Slide 15: x86 Page Table Walking
Core
Cache Hierarchy
Page Table
TLB
Main Memory
load VA1
TLB miss!
0xA0 | 0xA1 | 0xA2 | 0xA3 | 0xA4 | 0xA5 | 0xA6 | 0xA7
SE | PML4 offset | PDP offset | PD offset | PT offset | Page offset
PML4E
PDE
PDPE
CR3
PTE
virtual address space
…
…
Memory Hierarchy
L2
L1
LLC
DRAM

## Slide 16: Motivation for Exploiting Page Table Locality
0xA0 | 0xA1 | 0xA2 | 0xA3 | 0xA4 | 0xA5 | 0xA6 | 0xA7
SE | PML4 offset | PDP offset | PD offset | PT offset | Page offset
PML4E
PDE
PDPE
PTE of 0xA0
PTE of 0xA1
PTE of 0xA2
PTE of 0xA3
PTE of 0xA4
PTE of 0xA5
PTE of 0xA6
PTE of 0xA7
CR3
8 bytes

## Slide 17: Motivation for Exploiting Page Table Locality
0xA0 | 0xA1 | 0xA2 | 0xA3 | 0xA4 | 0xA5 | 0xA6 | 0xA7
SE | PML4 offset | PDP offset | PD offset | PT offset | Page offset
PML4E
PDE
PDPE
PTE of 0xA0
PTE of 0xA1
PTE of 0xA2
PTE of 0xA3
PTE of 0xA4
PTE of 0xA5
PTE of 0xA6
PTE of 0xA7
CR3
64 bytes

## Slide 18: Motivation for Exploiting Page Table Locality
0xA0 | 0xA1 | 0xA2 | 0xA3 | 0xA4 | 0xA5 | 0xA6 | 0xA7
SE | PML4 offset | PDP offset | PD offset | PT offset | Page offset
PML4E
PDE
PDPE
PTE of 0xA0
PTE of 0xA1
PTE of 0xA2
PTE of 0xA3
PTE of 0xA4
PTE of 0xA5
PTE of 0xA6
PTE of 0xA7
CR3
Cache Hierarchy
At the end of each page walk there are 7 PTEs that are prefetched for free
Prefetching all the free PTEs per page walk results in sub-optimal performance gains
TLB Prefetch
Queue

## Slide 19: Sampling-based Free TLB Prefetching (SBFP)
Prefetch only the useful free PTEs per page walk
Adapt to phase-based behaviors
Can be combined with any TLB prefetcher
Exploit page table locality for both demand and prefetch page walks

## Slide 20: Terminology
After a page table walk, 8 PTEs are stored into a cache line
Free Distance = signed distance between the PTE that holds the demand translation and another free PTE
  14 possible free distances, from -7 to +7 (excluding zero)
Assume a TLB miss for virtual page 0xA3
0xA0 | 0xA1 | 0xA2 | 0xA3 | 0xA4 | 0xA5 | 0xA6 | 0xA7
cache_position(0xA3) = 3
e.g., Free Distance(0xA0) = -3
0xA0 | 0xA1 | 0xA2 | 0xA3 | 0xA4 | 0xA5 | 0xA6 | 0xA7

## Slide 21: Sampling-based Free TLB Prefetching — Overview
C-7 | C-6 | C-5 | C-4 | C-3 | C-2 | C-1 | C+1 | C+2 | C+3 | C+4 | C+5 | C+6 | C+7
virtual page | physical page | free distance
virtual page | free distance
Prefetch Queue
Sampler
Free Distance Table (FDT)
saturating counters

## Slide 22: Sampling-based Free TLB Prefetching — Operation
0xA0 | 0xA1 | 0xA2 | 0xA3 | 0xA4 | 0xA5 | 0xA6 | 0xA7
C-7 | C-6 | C-5 | C-4 | C-3 | C-2 | C-1 | C+1 | C+2 | C+3 | C+4 | C+5 | C+6 | C+7
cache_position(0xA3) = 3
virtual page | physical page | free distance
0xA1 | 0xF1 | -2
0xA2 | 0xG2 | -1
0xA6 | 0xF6 | 3
virtual page | free distance
0xA4 | 1
0xA0 | -3
0xA5 | 4
0xA7 | 2
Threshold
Prefetch Queue
FDT
Sampler

## Slide 23: Sampling-based Free TLB Prefetching — Updating FDT
C-7 | C-6 | C-5 | C-4 | C-3 | C-2 | C-1 | C+1 | C+2 | C+3 | C+4 | C+5 | C+6 | C+7
Prefetch Queue
Sampler
Free Distance Table (FDT)
virtual page | physical page | free distance
0xA1 | 0xF1 | -2
0xA2 | 0xG2 | -1
0xA6 | 0xF6 | 3
virtual page | free distance
0xA4 | 1
0xA0 | -3
0xA5 | 4
0xA7 | 2

## Slide 24: Sampling-based Free TLB Prefetching — Updating FDT
C-7 | C-6 | C-5 | C-4 | C-3 | C-2 | C-1 | C+1 | C+2 | C+3 | C+4 | C+5 | C+6 | C+7
Prefetch Queue
Sampler
Free Distance Table (FDT)
virtual page | physical page | free distance
0xA1 | 0xF1 | -2
0xA2 | 0xG2 | -1
0xA6 | 0xF6 | 3
virtual page | free distance
0xA4 | 1
0xA0 | -3
0xA5 | 4
0xA7 | 2
++
++

## Slide 25: Combining SBFP with a TLB Prefetcher
Core
Cache Hierarchy
Page Table
TLB
Main Memory
Prefetch
Queue
TLB Prefetcher
Queue
VA1 —> PA17
load VA1
SBFP
FDT
Sampler

## Slide 26: Combining SBFP with a TLB Prefetcher
Core
Cache Hierarchy
Page Table
TLB
Main Memory
Prefetch
Queue
TLB Prefetcher
Queue
load VA1
Demand Page Walk
Miss!
Hit!
Prefetch Page Walk
SBFP
FDT
Sampler
++
TLB Miss!

## Slide 27: Agile TLB Prefetcher (ATP)
Core
Cache Hierarchy
Page Table
TLB
Main Memory
Prefetch
Queue
ATP
TLB Prefetcher
Queue

## Slide 28: Motivation for Agile TLB Prefetcher (ATP)
There is no state-of-the-art TLB prefetcher that performs best across all considered workloads
Different workloads correlate well with different features (e.g., strides, distances between virtual pages, PC)
When the TLB miss behavior is irregular, state-of-the-art TLB prefetchers issue useless prefetch requests

## Slide 29: Agile TLB Prefetcher (ATP)
Combine three low-cost TLB prefetchers
Adaptive selection logic and throttling mechanisms

## Slide 30: Constituent Prefetchers of ATP
Core
Cache Hierarchy
Page Table
TLB
Main Memory
Prefetch
Queue
ATP
STP
H2P
MASP

## Slide 31: Stride TLB Prefetcher (STP)
Core
Cache Hierarchy
Page Table
TLB
Main Memory
Prefetch
Queue
ATP
H2P
MASP
STP
vpn
vpn-2
vpn-1
vpn+1
vpn+2
STP targets TLB miss patterns that correlate well with small strides

## Slide 32: H2 Prefetcher (H2P)
Core
Cache Hierarchy
Page Table
TLB
Main Memory
Prefetch
Queue
ATP
STP
MASP
E + distance(E,D)
E + distance(D,A)
H2P detects miss patterns that correlate well with distances between virtual pages that produce TLB misses
TLB Miss Stream = …, A, D, E, …
H2P

## Slide 33: Modified Arbitrary Stride Prefetcher (MASP)
Core
Cache Hierarchy
Page Table
TLB
Main Memory
Prefetch
Queue
ATP
STP
H2P
PC | Previous VPN | Stride
More aggressive version of Arbitrary Stride Prefetcher (ASP)1
Assume a TLB miss for page A
  MASP prefetches the PTEs of the pages
    A + 5
    A + distance(A,E)
PC | Previous VPN | Stride
0xff | E | +5
1G. B. Kandiraju and A. Sivasubramaniam, "Going the Distance for TLB Prefetching: An Application-driven Study", ISCA'02

## Slide 34: Selection and Throttling Schemes
Core
Cache Hierarchy
Page Table
TLB
Main Memory
Prefetch
Queue
ATP
STP
H2P
MASP
Selection & Throttling Logic

## Slide 35: Selection and Throttling Schemes
Core
Cache Hierarchy
Page Table
TLB
Main Memory
Prefetch
Queue
ATP
STP
H2P
MASP
STP
H2P
MASP
FPQ
FPQ
FPQ
C0
C1
C2

## Slide 36: Agile TLB Prefetcher (ATP) — Operation
Core
Cache Hierarchy
Page Table
TLB
Main Memory
Prefetch
Queue
ATP
STP
H2P
MASP
FPQ
FPQ
FPQ
C0
C1
C2
load VA1
TLB miss

## Slide 37: Agile TLB Prefetcher (ATP) — Operation
Core
Cache Hierarchy
Page Table
TLB
Main Memory
Prefetch
Queue
load VA1
TLB miss
C0
C1
C2
Disable
STP
H2P
MASP

## Slide 38: Simulation Infrastructure
1https://github.com/ChampSim/ChampSim
ChampSim1
  Trace-driven multi-core out-of-order simulator
  x86 page table walker
Component | Parameters | Latency
L1 I-TLB | 64-entry, 8-way | 1cc
L1 D-TLB | 64-entry, 8-way | 1cc
L2 TLB | 1536-entry, 12-way | 8cc
Page Structure Caches | 3-level Split PSC, PML4: 2-entry, PDP: 4-entry, PD: 32-entry | 2cc
Prefetch Queue | 64-entry, fully assoc. | 2cc
Sampler | 64-entry, fully assoc | 2cc
L1 iCache | 32KB, 8-way | 1cc
L1 dCache | 32KB, 8-way | 1cc
L2 Cache | 256KB, 8-way | 8cc
LLC | 2MB/core, 16-way | 20cc
DRAM | 4GB, tRP=tRCD=tCAS=11 | variable

## Slide 39: Workloads
SPEC CPU 2006 benchmark suite
SPEC CPU 2017 benchmark suite
Industrial workloads provided by Qualcomm for Championship Value Prediction (CVP-1)
Big Data workloads
  GAP benchmark suite
  XSBench
SimPoint Methodology
TLB MPKI > 1

## Slide 40: State-of-the-art Data TLB Prefetchers1
Sequential Prefetcher (SP)
  Prefetch the PTE of the page located next to the one produced the TLB miss
Distance Prefetcher (DP)
  Distances between pages that produce consecutive TLB misses
Arbitrary Stride Prefetcher (ASP)
  PC-correlated prefetcher
1G. B. Kandiraju and A. Sivasubramaniam, "Going the Distance for TLB Prefetching: An Application-driven Study", ISCA'02

## Slide 41: Scenarios that Exploit Free TLB Prefetching
No Free TLB Prefetching (NoFP)
  Free prefetching is not exploited
Naive Free TLB Prefetching (NaiveFP)
  All free PTEs are stored into the PQ
Static Free TLB Prefetching (StaticFP)
  Static offline exploration of the overall most useful free distances per TLB prefetcher

## Slide 42: Performance Results

## Slide 43: Performance Results
The scenarios that exploit page table locality (NaiveFP, StaticFP, SBFP) significantly improve performance over NoFP

## Slide 44: Performance Results
SBFP provides larger speedups than the other scenarios that exploit page table locality across all evaluated TLB prefetchers

## Slide 45: Performance Results
ATP combined with SBFP provides the overall best speedups

## Slide 46: Performance Results
ATP+SBFP improves geomean performance by 16.2%, 11.1%, and 11.8% for the Qualcomm, SPEC, and Big Data workloads
ATP+SBFP outperforms the best already proposed TLB prefetcher by 8.7%, 3.4%, and 4.2% for the Qualcomm, SPEC, and Big Data workloads

## Slide 47: Page Walk Memory References
‘page walk memory reference’ is a reference to the memory hierarchy (L1, L2, LLC, DRAM) due to a page walk

## Slide 48: Page Walk Memory References
Large increase in page walk memory references when page table locality is not exploited (NoFP)

## Slide 49: Page Walk Memory References
The scenarios that exploit page table locality (NaiveFP, StaticFP, SBFP) significantly reduce the page walk memory references

## Slide 50: Page Walk Memory References
SBFP provides the highest reduction in page walk memory references across all evaluated TLB prefetchers

## Slide 51: Page Walk Memory References
ATP combined with SBFP provides the overall highest reduction in page walk memory references

## Slide 52: Page Walk Memory References
ATP+SBFP reduces the page walk memory references by 37%, 26%, and 5% for the Qualcomm, SPEC, and Big Data workloads, over a baseline without TLB prefetching

## Slide 53: Storage Overhead
SBFP requires 0.31KB of storage
ATP requires 1.68KB of storage
ATP combined with SBFP requires 1.99KB of storage
ATP combined with SBFP outperforms the ISO-storage1 scenario by more than 9% across all the benchmark suites
1L2-TLB is augmented with additional entries to match the storage budget of ATP+SBFP

## Slide 54: Additional Evaluation Results
Activation ratio of the constituent prefetchers of ATP
Portion of the PQ hits provided by ATP and SBFP
Performance improvement when 2MB pages are used
Dynamic energy consumption of address translation
Comparison with other approaches that improve TLB performance

## Slide 55: Conclusions
This work reduces the address translation overheads via TLB prefetching
  microarchitectural technique | relies on the memory access patterns | not disruptive
Our proposal
  Sampling-based Free TLB Prefetching (SBFP)
    Exploit page table locality to enhance the performance of prior and novel TLB prefetchers
  Agile TLB Prefetcher (ATP)
    Composite TLB prefetcher that combines three low-cost TLB prefetchers and disables prefetching when the TLB miss stream is irregular
Combining ATP with SBFP improves geomean performance by more than 10% across different benchmark suites and reduces most of the page walk references to the memory hierarchy

## Slide 56: Thank you!
georgios.vavouliotis@bsc.es