## Slide 1: Colored Huge Pages A Hardware-Software Approach for Enhanced Isolation and Performance
Georgios-Alexandros Kostas Dimitris Gizopoulos Vasileios Karakostas
University of Athens

## Slide 2: Page Coloring + Huge Pages (?)
When using huge pages:
Page Coloring + Huge Pages
Page Coloring: software approach for partitioning shared resources
  Bits of PFN can influence which portions of a shared resource a process can access
Huge Pages: improve virtual memory performance
  A single TLB entry provides address translation for a larger memory region
Page coloring and huge pages are incompatible
When using regular pages:

## Slide 3: Prior Work: Scattered Superpages
Problem: massive physical contiguity required
Scattered Superpages [ICCD’13]: break down physical huge page into individual base pages of the desired color:
Skip pages with colors other than the desired one

## Slide 4: Our Approach: Colored Huge Pages
CHP Components
Hardware: efficient translation with simple modifications in L2 TLB and Page Table Walker
Software: OS constructs and installs these mappings in process address space
Colored Huge Pages: allow each 2MB strided mapping to break down into multiple sub-mappings:
Each sub-mapping begins independently

## Slide 5: Enhanced L2 TLB
Challenge 1: need to hold 8 PFNs per CHP translation
Solution: widen each L2 TLB entry to fit 7 additional PFNs
  More silicon required but indexing time remains practically unaffected
Looked up after L1 TLB miss
Upon L2 TLB hit for a CHP, construct & install 4KB entry in L1 TLB
Only modify the L2 TLB

## Slide 6: Fetching CHP Translations
All 8 PFNs fit into one cache line
Challenge 2: need to retrieve 8 PFNs per CHP translation
Solution: retrieve all 8 PFNs with a single memory reference
  Fetching all 8 sub-mapping translations almost as cheap as fetching just one
…
PFN0
PFN1
PFN2
PFN3
PFN4
PFN5
PFN6
PFN7
…
64-byte cache line in the cache hierarchy
8 PFNs per CHP translation

## Slide 7: Address Translation with CHP
 Parallel Lookup
 VPN Extraction
Huge Page Offset
base page offset
VPN
Target PFN
huge offset
page_index * num_colors
 Sub-entry Index Calculation
+
 Final PFN Calculation
 Page Offset Computation
page index
 Sub-entry Extraction
Extended L2 TLB
PFN0
tag
PFN1
PFN7
flags
sub-map 0
sub-map 1
sub-map 7
V
num_colors is power of 2 
use shifts

## Slide 8: Evaluation
Huge Pages (THP):
21% speedup (up to 42.4%)
Chart: Speedup
| mcf | astar | omnetpp | bfs | tc | cc | Average
Contention, No coloring (4KB) | 1 | 1 | 1 | 1 | 1 | 1 | 1
Contention, No coloring (THP) | 1.047 | 1.09 | 1.097 | 1.424 | 1.073 | 1.416 | 1.21
Contention, Coloring (4KB) | 1.37 | 1.212 | 1.156 | 1.108 | 1.037 | 1.118 | 1.174
Colored Huge Pages | 1.41 | 1.291 | 1.241 | 1.453 | 1.102 | 1.456 | 1.337
Performance
Contention with 4KB Pages:
Baseline
Colored Huge Pages (CHP):
33.7% speedup (up to 45.6%)
Page Coloring:
17.4% speedup (up to 37%)
Linux kernel + analytical modeling

## Slide 9: Colored Huge Pages A Hardware-Software Approach for Enhanced Isolation and Performance
Georgios-Alexandros Kostas Dimitris Gizopoulos Vasileios Karakostas
University of Athens